## Slide 1: Project Work Phase-2 7th semester AY: 2026-27
Review 2 Presentation
Project Title: Enhancing Emergency Response Through IoT-Integrated Smart Ambulance and GPS Monitoring
Presented By
Rahul S (1NT23EC120)
Rakshita S Wagge (1NT23EC124)
Project Supervisor
Dr. Manjula B M
Professor
Dept. of Electronics and Communication Engineering
Nitte Meenakshi Institute of Technology, Yelahanka, Bangalore-560064

## Slide 2: Presentation Outline
Objectives
​Detailed Architecture & Design Finalization
Techniques/methods/approaches used for the proposed work
​Functional Requirements
​Non-Functional Requirements
Corresponding Test Scenarios
Test Cases to validate each requirement
Conclusion and Future Work

## Slide 3: Project Objectives
The following are the Finalized objectives of the project:
1. To develop a BLE-based mobile communication backbone for transmitting real-time patient vitals to a mobile application, which securely forwards data to the cloud using MQTT over TLS, with CoAP as a backup.
2. To integrate the existing patient health monitoring system with the mobile communication backbone for continuous vital acquisition, transmission, and remote monitoring during ambulance transit.
3. To implement RTOS-based concurrent task management for sensor acquisition, vital processing, communication, and local display, ensuring responsive and reliable operation.
4. To develop an ML-based patient risk prediction module that analyses real-time vitals, identifies potential deterioration, and classifies patient risk levels for early clinical assessment.

## Slide 4: Architecture

## Slide 5: BLE Communication Workflow
Scan for
Smart_Ambulance
Connect and
encrypt link
Discover GHSS
and subscribe
Send Start
command 0x01
Receive simulated
vital observations
Decode and display
HR, SpO2, temperature
After subscription, the app enables start/stop control
Stop: 0x02 Disconnect: ESP32 resumes advertising Reconnect: scan and select again
5
Notes: GHSS UUID 0x1840; observations 0x2B8B; control point 0x2BF4. Firmware creates simulated readings on a nominal one-second task interval. The two rows show setup followed by telemetry, with editable step objects. Automatic app reconnection is not implemented.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 6: Methods and Design Comparison
Design aspect | Current prototype | Target design
Device to phone | BLE notifications | Retain BLE gateway
Wide-area upload | Not implemented | MQTT/TLS with CoAP fallback
Data source | Simulated observations | Integrated physical sensors
Patient assessment | Vitals display | ML risk classification
Ambulance location | Not implemented | Phone GPS with ETA
BLE supports the local link. Cloud transports require phone internet connectivity.
6
Notes: Comparison describes observed implementation versus the user-approved target, without claiming measured superiority over competing protocols. No backend stack or risk model is finalized in the current repository.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 7: Functional Requirements
ID | Required behavior | Implementation
FR1 | Discover, connect and receive BLE vitals | Code present
FR2 | Start/stop telemetry from the app | Code present
FR3 | Acquire sensors and update local OLED | Integration pending
FR4 | Queue and upload telemetry to cloud | Planned
FR5 | Provide GPS location and ETA | Planned
FR6 | Predict risk and show hospital updates | Planned
7
Notes: FR1 and FR2 are implemented in source but need hardware evidence. Sensor sketches exist separately. Persistent queueing, cloud transport, GPS, ETA, ML and hospital dashboard are requirements for subsequent integration.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 8: Non-Functional Requirements
Quality | Acceptance check | Evidence needed
Security | Encrypted BLE before stream control | ESP32 encryption log
Responsiveness | Regular updates without a frozen UI | Timed recording and logs
Recovery | Resume telemetry after reconnect | Disconnect/reconnect recording
Data integrity | App values match transmitted values | Matched app and serial captures
Continuity | Retain unsent readings during outage | Future queue/retry test
Latency, endurance and reliability thresholds remain proposed until measured and agreed.
8
Notes: Security code uses LE Secure Connections with Just Works and NVS bonds. This does not establish authenticated protection against active interception. No measured latency, delivery ratio, endurance or clinical accuracy is available.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 9: Wi-Fi vs BLE: Design Rationale
Criterion | Earlier Wi-Fi approach | Selected BLE approach
Local connection | ESP32 joins access point or hotspot | ESP32 connects directly to phone
Internet gateway | ESP32 manages network uplink | Phone handles cloud uplink (planned)
Data workload | Supports higher data throughput | Fits small, periodic vital readings
Device setup | Configure SSID and password | Discover device and pair
Power rationale | Measure under the same workload | Low-power design; savings unmeasured
BLE fits the phone gateway design. Phone proximity remains a requirement.
9
Notes: Design rationale, not measured Wi-Fi versus BLE test results. The earlier project README describes direct ESP32 Wi-Fi MQTT/TLS upload. The current architecture moves internet upload, GPS and planned buffering to the phone, while BLE carries nearby vital observations. Wi-Fi also supports local communication without internet, and a phone hotspot can provide a Wi-Fi uplink. The selected design removes Wi-Fi credentials and cloud connection handling from the ESP32 local link; it does not establish better latency, reliability, range or measured power consumption. BLE is designed for low-power point-to-point data exchange, including health monitoring. A fair empirical comparison would use the same board, workload, distance and observation duration, recording current draw, delivery ratio, update interval and recovery time. Sources: https://www.bluetooth.com/learn-about-bluetooth/topology-options/ ; https://www.bluetooth.com/bluetooth-le-primer/ ; https://docs.espressif.com/projects/esp-idf/en/latest/esp32/api-reference/bluetooth/bt_le.html ; earlier project README at D:/Academ/Projects/Major Project 2026-27/Coding Part/Smart Ambulance/README.md.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 10: BLE Test Cases
Test | Action | Expected observation
TC1 / FR1 | Scan with ESP32 advertising | Smart_Ambulance appears
TC2 / FR1 | Select device and pair | Connected and ready status
TC3 / FR1 | Start telemetry | Vitals update and match logs
TC4 / FR2 | Tap Stop | Stop acknowledged; updates cease
TC5 / FR1 | Disconnect, then scan and connect | Telemetry can restart
Execution status: evidence pending. Capture the observed outcome before marking Pass.
10
Notes: These cases validate the current BLE prototype. Capture at least two updates for TC3, and a recording or timestamped logs for TC4 and TC5. A stopped app may retain the last displayed values. Reconnection is manual.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 11: Planned Integration Tests
Requirement | Test scenario | Expected result
FR3 / Sensors | Connect sensors and OLED | Correct acquisition and local display
FR4 / Upload | Lose and restore phone internet | Queue retained and uploaded once
FR5 / GPS + ETA | Move along a known route | Location and ETA update
FR6 / ML | Evaluate a labeled held-out dataset | Report classification metrics
FR6 / Dashboard | Deliver live and stale telemetry | Correct values and freshness state
All cases on this slide are planned. No cloud, GPS, ETA or ML results are claimed.
11
Notes: Future tests need a defined telemetry contract and acceptance thresholds. ETA should be compared with actual arrival times on test routes. ML evaluation requires a selected dataset, labels, model and held-out split. Do not invent accuracy figures.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 12: Implementation Status
Module | Current evidence | Remaining work
ESP32 BLE | Advertising, encryption, streaming code | Device validation evidence
Flutter app | Scan, connect, display, start/stop | Gateway persistence and uploads
Sensors / OLED | Separate sensor sketches | Integrate into BLE firmware
RTOS | BLE host and simulation tasks | Full acquisition/display pipeline
Cloud / Dashboard | Placeholder component folders | Implement and integrate
GPS / ETA / ML | No implementation found | Design, implement and evaluate
12
Notes: Main repository checked at D:/Academ/git-local/smart-ambulance. The older Coding Part/Smart Ambulance README describes a Wi-Fi/cloud design, but the inspected backend/frontend folders contain remnants rather than a complete current implementation. Status follows current source and the user confirmation, not older README claims.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 13: Prototype Evidence
Connected and ready
Screenshot pending
Simulated vitals streaming
Screenshot pending
Stopped or reconnected
Screenshot pending
Use real device captures. Pair the app display with matching ESP32 serial logs.
13
Notes: Evidence slots intentionally await user screenshots. Suggested captures: connected-ready status; streaming HR/SpO2/temperature; stopped status or successful manual reconnection. A recording must establish changing readings and cessation of updates. All readings in the current demonstration are simulated.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 14: Conclusion and Future Work
14
Implemented ESP32 BLE communication and a Flutter app for simulated vitals.
Supported device discovery, encrypted connection and start/stop control.
Integrate physical sensors, OLED and the full RTOS task pipeline.
Add persistent uploads, cloud services and the hospital dashboard.
Develop GPS tracking, ETA estimation and ML risk prediction.
Notes: Conclusions distinguish implemented code from demonstrated hardware results. The full system remains a prototype. ML risk assessment is a project objective and requires dataset/model selection and evaluation.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 15
Thank You
15
Notes: End of Review 2 presentation.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.