## Slide 1
BLE Architecture: Flutter to ESP32
Generic Health Sensor Service (GHSS): 0x1840
Flutter app
BLE central / GATT client
Encrypted BLE connection
ESP32
BLE peripheral / GATT server
Start / Stop
commands
GHS Control Point
0x2BF4
Write and indicate
Validate command
Enable / disable
telemetry stream
Decode and display
HR, SpO2, temperature
Live Observations
0x2B8B
Notifications
Simulated vitals task
Encode observations
ESP32 returns command acknowledgements through control-point indications
Setup: scan, connect, pair, discover GHSS and subscribe
Dept. of Electronics and Communication Engineering, NMIT, Bengaluru
Notes: Architecture of the implemented ESP32-to-phone BLE prototype. The Flutter app is the BLE central/GATT client. ESP32 advertises as Smart_Ambulance and hosts GHSS 0x1840. App start 0x01 and stop 0x02 commands use control point 0x2BF4. Firmware requires link encryption and subscribed indications, validates the command, sets stream state, and indicates acknowledgement 0x80. The simulated-vitals task emits heart rate, SpO2 and temperature observations through notifications on 0x2B8B. Physical sensor integration is planned. Sources: current app/lib/main.dart and esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c.