## Slide 1: Project Work Phase-2 7th semester AY: 2026-27
Review 2 Presentation
Enhancing Emergency Response Through IoT-Integrated
Smart Ambulance and GPS Monitoring
Rahul S (1NT23EC120) Rakshita S Wagge (1NT23EC124)
Project Supervisor
Dr. Manjula B M, Professor
Department of Electronics and Communication Engineering
Nitte Meenakshi Institute of Technology, Bengaluru
1
Notes: Project title and team details retained from the supplied Review 2 template.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 2: Presentation Outline
1. Objectives and system architecture
2. BLE workflow and design comparison
3. Requirements and validation plan
4. Implementation status and evidence
5. Conclusion and future work
2
Notes: Review 2 topics follow the supplied template. Additional slides separate methods, validation and evidence to keep each slide concise.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 3: Project Objectives
Communication
BLE gateway with MQTT over TLS and CoAP fallback
Monitoring
Integrate patient sensors and local display
Concurrency
Coordinate acquisition and communication using RTOS
Risk assessment
Develop ML classification of patient deterioration
Location and ETA
Track ambulance location and estimate arrival time
3
Notes: Objectives preserve the template scope. User explicitly retained ML as an objective and added both GPS location and ETA. These are objectives, not completed results.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 4: System Architecture
Patient sensors
Integration planned
ESP32
BLE implemented
Flutter gateway
BLE implemented
OLED and full RTOS pipeline: planned
Cloud ingestion
and storage
ML risk assessment
Hospital dashboard
Phone GPS and ETA: planned gateway functions
Filled blocks: current BLE prototype Outlined blocks: planned integration
4
Notes: Target architecture replaces the dense source image with an editable diagram. Current firmware generates simulated observations. Planned phone-to-cloud transport is MQTT over TLS with CoAP fallback. GPS provider, ETA method, backend and ML model remain to be selected.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 5: BLE Communication Workflow
Scan for
Smart_Ambulance
Connect and
encrypt link
Discover GHSS
and subscribe
Send Start
command 0x01
Receive simulated
vital observations
Decode and display
HR, SpO2, temperature
After subscription, the app enables start/stop control
Stop: 0x02 Disconnect: ESP32 resumes advertising Reconnect: scan and select again
5
Notes: GHSS UUID 0x1840; observations 0x2B8B; control point 0x2BF4. Firmware creates simulated readings on a nominal one-second task interval. The two rows show setup followed by telemetry, with editable step objects. Automatic app reconnection is not implemented.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 6: Methods and Design Comparison
Design aspect | Current prototype | Target design
Device to phone | BLE notifications | Retain BLE gateway
Wide-area upload | Not implemented | MQTT/TLS with CoAP fallback
Data source | Simulated observations | Integrated physical sensors
Patient assessment | Vitals display | ML risk classification
Ambulance location | Not implemented | Phone GPS with ETA
BLE supports the local link. Cloud transports require phone internet connectivity.
6
Notes: Comparison describes observed implementation versus the user-approved target, without claiming measured superiority over competing protocols. No backend stack or risk model is finalized in the current repository.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 7: Functional Requirements
ID | Required behavior | Implementation
FR1 | Discover, connect and receive BLE vitals | Code present
FR2 | Start/stop telemetry from the app | Code present
FR3 | Acquire sensors and update local OLED | Integration pending
FR4 | Queue and upload telemetry to cloud | Planned
FR5 | Provide GPS location and ETA | Planned
FR6 | Predict risk and show hospital updates | Planned
7
Notes: FR1 and FR2 are implemented in source but need hardware evidence. Sensor sketches exist separately. Persistent queueing, cloud transport, GPS, ETA, ML and hospital dashboard are requirements for subsequent integration.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 8: Non-Functional Requirements
Quality | Acceptance check | Evidence needed
Security | Encrypted BLE before stream control | ESP32 encryption log
Responsiveness | Regular updates without a frozen UI | Timed recording and logs
Recovery | Resume telemetry after reconnect | Disconnect/reconnect recording
Data integrity | App values match transmitted values | Matched app and serial captures
Continuity | Retain unsent readings during outage | Future queue/retry test
Latency, endurance and reliability thresholds remain proposed until measured and agreed.
8
Notes: Security code uses LE Secure Connections with Just Works and NVS bonds. This does not establish authenticated protection against active interception. No measured latency, delivery ratio, endurance or clinical accuracy is available.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 9: BLE Test Cases
Test | Action | Expected observation
TC1 / FR1 | Scan with ESP32 advertising | Smart_Ambulance appears
TC2 / FR1 | Select device and pair | Connected and ready status
TC3 / FR1 | Start telemetry | Vitals update and match logs
TC4 / FR2 | Tap Stop | Stop acknowledged; updates cease
TC5 / FR1 | Disconnect, then scan and connect | Telemetry can restart
Execution status: evidence pending. Capture the observed outcome before marking Pass.
9
Notes: These cases validate the current BLE prototype. Capture at least two updates for TC3, and a recording or timestamped logs for TC4 and TC5. A stopped app may retain the last displayed values. Reconnection is manual.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 10: Planned Integration Tests
Requirement | Test scenario | Expected result
FR3 / Sensors | Connect sensors and OLED | Correct acquisition and local display
FR4 / Upload | Lose and restore phone internet | Queue retained and uploaded once
FR5 / GPS + ETA | Move along a known route | Location and ETA update
FR6 / ML | Evaluate a labeled held-out dataset | Report classification metrics
FR6 / Dashboard | Deliver live and stale telemetry | Correct values and freshness state
All cases on this slide are planned. No cloud, GPS, ETA or ML results are claimed.
10
Notes: Future tests need a defined telemetry contract and acceptance thresholds. ETA should be compared with actual arrival times on test routes. ML evaluation requires a selected dataset, labels, model and held-out split. Do not invent accuracy figures.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 11: Implementation Status
Module | Current evidence | Remaining work
ESP32 BLE | Advertising, encryption, streaming code | Device validation evidence
Flutter app | Scan, connect, display, start/stop | Gateway persistence and uploads
Sensors / OLED | Separate sensor sketches | Integrate into BLE firmware
RTOS | BLE host and simulation tasks | Full acquisition/display pipeline
Cloud / Dashboard | Placeholder component folders | Implement and integrate
GPS / ETA / ML | No implementation found | Design, implement and evaluate
11
Notes: Main repository checked at D:/Academ/git-local/smart-ambulance. The older Coding Part/Smart Ambulance README describes a Wi-Fi/cloud design, but the inspected backend/frontend folders contain remnants rather than a complete current implementation. Status follows current source and the user confirmation, not older README claims.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 12: Prototype Evidence
Connected and ready
Screenshot pending
Simulated vitals streaming
Screenshot pending
Stopped or reconnected
Screenshot pending
Use real device captures. Pair the app display with matching ESP32 serial logs.
12
Notes: Evidence slots intentionally await user screenshots. Suggested captures: connected-ready status; streaming HR/SpO2/temperature; stopped status or successful manual reconnection. A recording must establish changing readings and cessation of updates. All readings in the current demonstration are simulated.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 13: Conclusion and Future Work
Current implementation
ESP32 BLE and Flutter gateway code support
simulated vital streaming with start/stop control
Sensor and OLED
integration
Persistent uploads
and cloud
GPS location
and ETA
ML risk assessment
and dashboard
Next validation: capture BLE evidence, then integrate and test the remaining modules.
13
Notes: Conclusions distinguish implemented code from demonstrated hardware results. The full system remains a prototype. ML risk assessment is a project objective and requires dataset/model selection and evaluation.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.

## Slide 14
Thank You
14
Notes: End of Review 2 presentation.
Sources: current workspace app/lib/main.dart; esp32/components/ble/ble.c, ble_gap.c, ble_gatt.c; esp32/main/main.c. Repository inspection on 19 October 2026. Code presence establishes implementation only. Hardware test outcomes await captured evidence.